## Slide 1: MovAlyzeR Features (Extracted features)
Trial, Segmentations, Strokes
Segmentation 1
Segmentation 2
Segmentation 3
Stroke 2
Stroke 1
Trial 1

## Slide 2: 1a. Static (Shape) Features
Absolute Size
Trace Length
Vertical Start Position
Vertical Size
Horizontal Size
Positions and sizes (cm)
Horizontal Start Position

## Slide 3: 1b. Static (Shape) Features
Slant
Slant (radians)*
Relative Initial Slant (radians) during first 80 ms*
Rel. Initial Slant
* Radian = Arc length / Radius
1 radian = 57 degrees
Notes: Shape features:
o Direction of the entire stroke
o Direction of the beginning of the stroke

## Slide 4: 1c. Static (Shape) Features
Straightness Error (cm)
Straightness Error = Average distance to minimum RMS distance line
Notes: Straightness of a stroke

## Slide 5: 1d. Static (Shape) Features
Loop surface between successive strokes (cm2)
Loop Surface
Notes: Enclosed surface of a loop

## Slide 6: 2. Dynamic Features
Duration
Peak y Velocity
Start Time
6
6
Y Position (cm)
Y Velocity (cm/s)

## Slide 7: 2a. Dynamic Features
Peak y Acceleration
(=Largest absolute of pos. and neg. acceleration within 1 stroke)
Average Absolute y Jerk
7
7
Y Position (cm)
Y Velocity (cm/s)
Y Acceleration (cm/s2)
Y Jerk (cm/s3)

## Slide 8: 2b. Dynamic Features
Average Pressure*
Average Absolute Jerk (cm/s3)
8
8
* Unit is tablet’s pressure units

## Slide 9: 3a. Dysfluency Features
Normalized jerk per Stroke~
{½ * ∫dt Jerk2(t) } * duration5 / size2
Units: s1 (cm1 / s -3)2 s5 cm-2 = Unit free
A maximally smooth, straight harmonic stroke yields 7.75 (π3/22).
A perfectly circular, constant-velocity stroke yields 10.96 (π3/21.5).
~Teulings, H.L., Contreras-Vidal, J.L., Stelmach, G.E., and Adler, C.H. (1997). Coordination of fingers, wrist, and arm in Parkinsonian handwriting. Experimental Neurology, 146, 159-170.
Notes: Enclosed surface of a loop

## Slide 10: 3b. Dysfluency Features
Number of Peak Acceleration Points per Stroke
Frequency of Secondary Submovements
Relative Duration of Primary Submovement
Relative Size of Primary Submovement

## Slide 11: 3c. Dysfluency Features
11
11
Relative Time To Peak y Velocity = Time to Peak / Duration
11
3/23/2016
11
Y Position (cm)
Y Velocity (cm/s)
Time To Peak
Duration

## Slide 12: 4. Additional Features
Plug-ins (MovAlyzeR “External Apps”)
  Batch file, calling any executable
  Matlab script
Notes: Enclosed surface of a loop